Compliant leg design for ideal airdrop
To avoid the use of parachutes and other attenation systems we now have to introduce something new to our bots.
To implement this there are severel tecniques, and some of them are~
- Active damping- Here we manually control the the leg of the bot and hence can absorb the shock of drop by bending knees ,etc.
  But it’s as harder to implement than it’s easy to hear.Here the landing time is very less and is of the order 10-3 s and the impact time of landing is a fraction of it.So in this small time interval it,s very hard to control the movement of the knee. So there is great chance that the bot might receive a huge shock and it’s chances of breaking is very high.
- Passive damping- It involves use of compliant legs in order to reduce the shock during landing.Here compliant actuators connect actuators and limbs with springs, dampers, or strings to allow limbs to move during impact without applying controls.
  So this method is quit effective and couls be used practically for air-dropping robots.
- By changing it’s body posture- As the heading suggests in this method the shock on robot can be reduced by just by rolling the bot after landing to distribute the impact throughout it’s body;or by changing bot’s center of mass; etc.
  This method is also good but has some limitatons at the same time. If air-droping is being done on mountain region where there is an incline the rolling could cause the robot to topple. And hence it could have damage.
Now proceding with the method of passive damping, there are many ways to implement it~
- One segment(1S)
- Two-segment compliant structure (2SCS)
- Two-segment compliant joint (2SCJ)
- Three-segment(3S)
One Segment(1S)
It’s like a pogo stick. It does not have a knee and its length is directly affected by a spring, which its length is set by pulling a string that is connected to a pulley. But in this model once there is an impact the system becomes unstable and system energy could not be stablised.
Two-segment compliant structure (2SCS)
This sytem can also be analysed as the above one.
Two-segment compliant joint (2SCJ)
In this the optimal minimun acceleration is around 110m/s2 .
3 segment(3S)
This is a better technique as the optimal minium acceleration for this case is around 65 m/s2 which is less than that of 2SCJ. Now if compare the optimal minimun acceleration with 1S or 2SCS model than they seem to be better but in both 1S and 2SCS the load on knee servos is very high which is dangerous when the bot operated near servo limits in sticky surfaces.

If we are using the 3S model of compliant legs than to manufacture the parts 3D-printed polylactic
acid (PLA) parts, as it is relatively straightforward to construct a 3S configuration with 3D printed plastic parts and it is also cost efficient.

So the best way for air dropping is use of passive damping which could also change its body posture
and hence reduce the impact to very less.

Thanks